## Slide 1: Robot Floor Cleaner
Vacuum and Mop

## Slide 2: Overview
Design a robotic vacuum cleaner equipped with omnidirectional wheels, capable of smoothly traversing doorway thresholds between rooms and onto balconies.
The design must accommodate challenging electrical conditions—particularly in rural India, where frequent power outages and voltage fluctuations occur.
The vacuum must maintain operational continuity during brief interruptions and be capable of quickly reconnecting when power is restored.

## Slide 3: Key Design Requirements
Power Reliability:
Must withstand power fluctuations and outages without losing operational memory or requiring manual resets.
Should include a small onboard backup battery or capacitor system to manage brief outages or transitions.
Compact and Accessible Design:
Designed to navigate and clean beneath immovable furniture with a low-profile chassis.
Must reach tight spaces with consistent suction performance and adequate clearance.
Repairability and Local Sustainability:
The vacuum should be easily repairable using locally available components.
Clear modular assembly instructions should be included to facilitate quick replacement of parts.

## Slide 4
Obstacle and Threshold Navigation
Threshold Crossing Mechanism:
Inspired by excavators navigating obstacles like water pipes, the vacuum must cross thresholds through one of the following:
Automated System: Deployable jack stands integrated into the casing, activated at a 90-degree angle when a threshold is detected.
Manual Guidance: Visual guides or diagrams printed on the vacuum shell to help the user reposition it manually if needed.
Doorway Threshold Specifications:
Length: 74 cm (±7 cm)
Height 1: 5 cm (+1.5 cm)
Width: 7 cm (+1.5 cm)
Height 2: 4.5 cm (+1 cm to -0.5 cm)
Note: A 3.4 cm vertical drop exists midway, requiring adaptive elevation response.

## Slide 5: Cleaning Capabilities
Indoor Debris Collection:
Must efficiently clean dust, sand, vegetable leaves, kitchen waste, oil stains, and paint flakes often found in older rural homes.
Outdoor (Balcony) Debris Handling:
Should handle leaves, pests, accumulated dust, and sand, and adapt to varying surfaces and debris density.

## Slide 6: Obstacle Recognition & AI Integration
Movable Object Handling:
Must identify and alert the user about objects like chairs, pedestal fans, and wires via a small built-in alarm.
If no response is detected after several attempts, the vacuum should resume cleaning and revisit the area later.
AI Functionality:
Use AI and vision systems to differentiate between movable and immovable objects.
Store object data to enhance path planning and cleaning efficiency over time.

## Slide 7: Optional Performance Enhancements
Wheel Design:
Add textured wheel surfaces (similar to golf ball dimples) to improve grip and prevent dust accumulation.
Avoid excessively smooth surfaces like those on computer mice, which attract dust and reduce efficiency over time.

## Slide 8: Furniture Clearance Constraints
Under-table Cleaning Specifications:
Wall to table-end width: 40 cm (+7 cm)
Table length: 240 cm (±10 cm)
Available cleaning clearance: 3.5 cm (−0.5 cm)
The vacuum must be able to clean this narrow space efficiently without getting stuck.

## Slide 9: Suggested Additions / Improvements:
Battery Backup or Failover Power: Add a brief UPS or smart capacitor to handle rural power flickers.
Dustbin Modularity: Detachable dustbins with easy-clean hatches.
Companion App (Optional): To receive alerts, manually mark obstacles, or schedule cleaning sessions.
Waterproofing (at least IPX4): Especially useful for cleaning balcony edges and kitchens.

## Slide 10: Improvements for Rural Development Context
Rugged Terrain Adaptability
Missing Feature: No mention of uneven floor surfaces, such as cracked cement, tiles with missing corners, or sloped floors, which are common in rural homes.
Improvement:
Add suspension-based wheel modules or adaptive wheel elevation.
Use infrared or pressure sensors to detect floor dips and auto-adjust suction/nozzle height.

## Slide 11: Localized Dust and Dirt Profiles
Missing Feature: Lack of emphasis on natural and agricultural residues (e.g., mud, dry grain husks, cow dung particles, firewood debris).
Improvement:
Include customizable cleaning modes for rural homes.
Design filters and dustbins for larger, fibrous, or sticky materials.

## Slide 12: Multi-surface Transition Capability
Missing Feature: No mention of transitioning between surfaces like mud-to-tile, tile-to-wood, or stone-to-cement.
Improvement:
Smart traction control based on detected surface type.
Automatic suction modulation for different surfaces.

## Slide 13: Extended Power Backup or Manual Mode
Missing Feature: Only brief power backup mentioned; not adequate in areas with long outages.
Improvement:
Add a swappable battery or solar charging option.
Introduce a manual push-clean mode that can still sweep or brush without electronics during long outages.

## Slide 14: User-Desirable Features (Currently Missing) - Voice and Language Support
Missing Feature: No mention of interface usability for non-tech-savvy users.
Improvement:
Add voice alerts or control in local languages (Hindi, Tamil, Telugu, etc.).
Use simple icons and color indicators instead of complex apps.

## Slide 15: User-Desirable Features (Currently Missing) - Waste Segregation
Missing Feature: No support for separating wet and dry waste, which can aid hygiene and composting.
Improvement:
Implement dual-compartment dustbins with different filters for wet/dry matter.

## Slide 16: User-Desirable Features (Currently Missing) - Remote Notification Without Wi-Fi
Missing Feature: No alternative if Wi-Fi is unavailable.
Improvement:
Add offline SMS-based alerts or Bluetooth-only app connectivity.

## Slide 17: Maintenance and Hygiene Improvements - Self-cleaning Brushes or Auto-Flush Option
Missing Feature: No mention of self-cleaning features, crucial when cleaning sticky waste.
Improvement:
Include removable, washable brush heads or auto-cleaning bristles with a rinse tank.

## Slide 18: Maintenance and Hygiene Improvements - Rodent- and Insect-Resistant Casing
Missing Feature: Rural homes may have more pests, which could damage wiring or sensors.
Improvement:
Use sealed compartments and pest-resistant outer materials.
Ensure ventilation without easy access for insects.

## Slide 19: Smart Learning Improvements - Local Map Storage
Missing Feature: No offline mapping.
Improvement:
Enable the device to build and store maps locally, even without cloud sync.
Include offline firmware updates via USB or Bluetooth.

## Slide 20: Smart Learning Improvements - Multi-User Awareness or Schedule Sharing
Missing Feature: No mention of multiple users in joint-family homes.
Improvement:
Add user profiles or shared scheduling for large families.

## Slide 21: Miniature Cleaning Arm / Built-in Gap Cleaner Module - Identified Gap
Current design mentions 3.5 cm clearance under immovable furniture like tables, but no mechanism is included to clean within narrower spaces (e.g., 3 cm height clearance).
Width from wall to table end: 40 cm, which is hard to access manually or with standard vacuum body.

## Slide 22: Proposed Solution: Integrated Micro-Cleaning Module
A built-in, retractable mini-cleaner designed to extend from the main body to clean narrow gaps such as:
Behind furniture near walls
Under extremely low-profile sofas/tables
Between wall fixtures or cabinetry

## Slide 23: Added Value in Rural Homes
Handles dust-prone nooks, especially in homes where furniture is rarely moved
Cleans kitchen corners, under traditional wooden beds, or around low-rise platforms
Saves elderly users from the hassle of reaching tough areas